## Slide 1: How to Power Direct Air Capture? Modeling System Wide Emissions Reduction of Direct Air Capture with Thermal Energy Storage
Vinay Konuru1, Aniruddh Mohan2, Kelsey Hatzell2, Jesse Jenkins2
Background and Context
Experimental Setup
Direct-Air Carbon Capture (DAC) is one of the lowest cost technologies to decarbonizing hard-to-abate industries
Question: How do we consistently supply clean power and heat?
Hypothesis: Thermal Energy Storage can reduce operational emissions by storing clean heat
Technical constraints: 100C sorbent regeneration
Economic constraints: High capital cost, low flexibility
Policy constraints: CO2 Capture Targets
Plant Design Configurations
TES
4
3
2
1
System
  ERCOT
  2-Zone System
  DAC in East Texas
Plant
  Solid Sorbent
  Grid-Connected
  1MtCO2 Annual Capacity
Key finding 3: System emissions reductions are driven by reductions in TES capacity cost
Key finding 2: System level cost of CO2 capture is reduced by $300/tCO2 with TES
Chart: DAC CO2 Removal Costs of Plant Versus System
| Grid HP | Grid HP + TES | TES | TES+Turbine
Plant Cost Per tCO2 | 842 | 842 | 980 | 996
System Cost Per tCO2 | 1035 | 988 | 734 | 620
System Penalty | 193 | 146 | -246 | -376
Key finding 1: Plant level cost of CO2 capture is reduced by $100/tCO2 with TES
Heat Pump Pros: Low fixed costs High heat generation efficiency Cons: No flexibility | Thermal Energy Storage Pros: Flexibility in heat production Cons: High fixed costs
Heat Pump + Thermal Energy Storage Pros: Smaller TES Cons: Lower heat storage capacity | Thermal Energy Storage + Turbine Pros: Energy security Cons: High fixed costs
Technology Overview
Chart: System Emissions Reduction (MtCO2)
| Grid HP | Grid HP + TES | TES | TES + Turbine
Emissions Reduction (MtCO2) | 0.81395 | 0.853 | 1.3345 | 1.6071
Chart: Plant Level Cost of Capture ($/tCO2)
| Grid HP | Grid HP + TES | TES | TES + Turbine
Fixed Costs | 808.7043 | 812.3036 | 870.9178 | 924.3272
Heat Costs | 33.4089 | 30.4605 | 51.343 | 40.2438
Power Costs | 11.6372 | 11.6372 | 11.6372 | 8.3292
Conclusion & Future Work
Key Findings
Overview
In this study, we’ve explored the capability of thermal energy storage to reduce the operational emissions and increase the system-wide emissions reductions of DAC plant by answering the following questions:
How do the plant-level cost of DAC increase with co-locating TES relative to other heating solutions?
To what degree do the system-wide emissions change in systems with DAC co-located with TES?
How would cost reductions in TES drive the synergy between these technologies?
Thermal energy storage shows great potential for improving the system-wide emissions reductions of DAC, but policy regulations will need to motivate the development of co-located DAC + TES plants to help overcome the early high plant level costs. This can be done through tax incentives or renewable energy procurement rules, which are meaningful areas for future research.
1. Department of Electrical and Computer Engineering, Princeton University
2. Andlinger Center for Energy and the Environment, Princeton University
Gas + Grid
+
DAC